## Slide 1: Number Representation: Unsigned, Signed, 2’s Compliment and Hexadecimal
Week 1
CSIS 2810

## Slide 2: Broad Course Overview
Everything in the computer is 1’s and 0’s
Two driving questions:
  How to convert Java programs to 1’s and 0’s
  How to build a circuit to interpret 1’s and 0’s
Levels of abstraction
  Key theme uniting these topics
A variety of miscellaneous topics

## Slide 3: From Java to 1’s and 0’s
Focus on fundamental concepts:
  Numbers, characters, strings
  Parameters and Procedures (inc. IO)
  Loops
  Arrays
Will often ignore
  OOP, GUI, etc.
Focus on numbers and instructions

## Slide 4: Bits and Bytes
Each 1 or 0 is the presence or absence of an electrical charge
This is called a bit
There are 8 bits in a byte
There are 32 bits (or 4 bytes) in a MIPS word
1024 bytes = 210 bytes = 1 Kilobyte (KB)
1024 KB = 220 bytes = 1 Megabyte (MB)
1024 MB = 230 bytes = 1 Gigabyte (GB)
1024 GB = 240 bytes = 1 Terabyte (TB)

## Slide 5: Bases and Symbols
Number of symbols needed is the number of the base
Base 10: 0,1,2,3,4,5,6,7,8,9
Base 2: 0,1
Base 8(octal): 0,1,2,3,4,5,6,7
Base 16(hex): 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F

## Slide 6: Base 10 Numbers
102 101 100
100 10 1

## Slide 7: Example: 143
102 101 100
100 10 1
1 4 3

## Slide 8: Base 10 → Base 2
27 26 25 24 23 22 21 20
107 106 105 104 103 102 101 100
↓

## Slide 9: Base 2 Numbers
27 26 25 24 23 22 21 20
128 64 32 16 8 4 2 1

## Slide 10: Example: 143
27 26 25 24 23 22 21 20
128 64 32 16 8 4 2 1
1 0 0 0 1 1 1 1
Count to 31 on one hand to practice binary counting

## Slide 11: Example B: 78
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 12: You Try: Value is 104

## Slide 13: Unsigned/Signed Representation
Unsigned
  The approach we’ve used so far
  Cannot represent negative numbers
  + Represents more positive numbers
Sign magnitude(historically important/used for floats)
  Use one extra bit for sign, 0 is +, 1 is -
  Where to put sign bit?(typically on left end of value)
  Extra step to calculate sign bit
  Positive and Negative value for zero
    What are they?
  Difficult for hardware designers
Can you represent 104 and/ or 143 as positive and/or negative values in sign magnitude format(8 bit)?

## Slide 14: You Try: 143 and 104
Decimal | Sign Magnitude (8 bit)
104 | 
-104 | 
143 | 
-143 | 

## Slide 15: Two’s Compliment
Two’s Compliment
  + Fixes most problems of sign magnitude
  One more negative value than positive value
To make a negative value positive, invert all the bits and add 1.
To make a positive value negative, invert all the bits and add 1.
Sign Extension
  Pad positive numbers with 0’s on the left
  Pad negative numbers with 1’s on the left

## Slide 16: You Try: 104 and 143
Decimal | Two’s Compliment (8 bit)
104 | 
-104 | 
143 | 
-143 | 

## Slide 17: 2’s Compliment Addition
Like traditional Base 10 addition
Add and carry
Signs will take care of themselves
  Unless signs of far left 2 bits do not match–
  if those signs don’t match, you have overflow!
Example:
  10011110
  +00101100
  ___________

## Slide 18: Comparing Binary Representations
Representation | Range | Values
Unsigned | 0 : 2n -1 | 2n
Sign Magnitude | -2n-1 -1 : 2n-1-1 | 2n-1
2’s Compliment | -2n-1 : 2n-1-1 | 2n
n Is the number of bits in the number
In class, generally n will be either 4, 8, 16, or 32
Underflow: If number is smaller than range
Overflow: If number is bigger than range

## Slide 19: Hexadecimal
More compact representation for humans
Used a lot later in the course
Memorize the 16 conversions
0 | 0000 | 4 | 0100 | 8 | 1000 | C | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | D | 1101
2 | 0010 | 6 | 0110 | A | 1010 | E | 1110
3 | 0011 | 7 | 0111 | B | 1011 | F | 1111

## Slide 20: Exit Question
Decimal | Unsigned | Signed | Two’s Comp. | Hex
42 |  |  |  | 
-42 |  |  |  |