## Slide 1: An Assembly Language and Instruction Set Architecture
Week 3 & 4
CSIS 2810

## Slide 2: General Architecture
Program Counter | Register File | Arithmetic Logic Unit | Memory
Contains Instructions Emits next instruction | Contains registers Fast,volatile, limited memory | Does the math Add, sub, and,or | Contains more, slower, non-volatile data memory.
PC
RF
ALU
MEM

## Slide 3: What is Assembly?
Assembly language is an intermediate level of abstraction between a higher level programming language and machine language(e.g. the 1’s and 0’s)
Java, C, etc.
Compiler
Assembly
Assembler
Machine Language
1’s and 0’s

## Slide 4: What is MIPS?
An assembly language
  Popular for educational purposes
  Used in embedded systems such as
    Routers, PlayStation, NEC
An acronym
  Microprocessor without Interlocked Pipelined Stages
  We will discuss a pipeline at end of course
A Reduced Instruction Set Computer(RISC)
  Instruction Set Architecture(ISA)

## Slide 5: What is an Instruction Set Architecture?
A set of instruction types and instructions that runs on a microprocessor
General Feature | Feature in MIPS
Instruction Types | R-Type, I-Type, J-Type
Instruction | Math, Memory, Control, etc.
Registers (Fast, available memory) | 32 registers
Addressing Modes | Several
Memory Architecture(slower memory) | 2 memories, one instruction + one data
Interrupt Exception Handling | Some, but often beyond scope of class
External IO | System calls
OpCodes and FunctCodes | Covered with instructions

## Slide 6: Design Principles
When designing an instruction set architecture(ISA)
  Simplicity favors regularity
  Smaller is faster
  Make the common case fast
  Good design demands good compromises

## Slide 7: Instruction Types
R type or R format (register format)
I type or I format (immediate format)
J type or J format(jump format)
6 bits opcode | 26 bits target address
6 bits opcode| 5 bits $rs | 5 bits $rt | 16 bits immediate
6 bits opcode| 5 bits $rs | 5 bits $rt |5 bits $rd |5 bits shamt| 6 bits funct

## Slide 8: You try!
Write a MIPS instruction to add the values in registers 6 and 9 and store the value in register 19.
  Convert to binary and hex!

## Slide 9: MIPS Memory and Assignment
Read from Memory(memory -> register)
  lw $s1, 12($s2)
  Like a=b[12];
Write to Memory (register-> memory)
  sw $s1, 12($s2)
  Like b[12]=a;
Load a constant
  li $s1, 9
  Like a=9;
PC
RF
ALU
MEM

## Slide 10: You try!
Write a MIPS instruction that loads a value from memory location 5 into register 8.
  Convert to binary and hex!
Write a MIPS instruction to store the value in register 21 to memory location 17.
  Convert to binary and hex.

## Slide 11: 7 Instructions to Implement
Assembly Code | Args | Format | Opcode/Funct Code
lw | $rt, imm($rs) | Opcode, rs, rt, imm | 100011/none
sw | $rt, imm($rs) | Opcode, rs, rt, imm | 101011/none
add | $rd, $rs, $rt | Opcode, rs, rt, rd, shamt, funct | 000000/100000
sub | $rd, $rs, $rt | Opcode, rs, rt, rd, shamt, funct | 000000/100010
and | $rd, $rs, $rt | Opcode, rs, rt, rd, shamt, funct | 000000/100100
or | $rd, $rs, $rt | Opcode, rs, rt, rd, shamt, funct | 000000/100101
j | Address | Opcode,address | none